## Slide 1: GPU-Accelerated Ray-Tracing Methods for Determining Radiation View Factors in Multi-Junction Thermoelectric Generators
Asher J. Hancocka and:
Laura B. Fulton, Justin Ying, Shervin Sammak, Ph.D.,
Matthew M. Barry, Ph.D
Department of Mechanical and Materials Science, UPitt
School of Computer Science, CMU
Department of Computer Engineering, UPitt
Center for Research Computing, UPitt
ajh172@pitt.edua

## Slide 2: Background: Thermoelectric generators and uses
Thermoelectric generators (TEGs) are solid-state energy conversion devices
Show promise in space applications, as well as the automobile industries
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
“Recent development and application of thermoelectric generator and cooler” () in Applied Energy
“US space radioisotope power systems and applications: past, present and future” () in Radioisotopes-Applications in Physical Sciences
Notes: TEGs have direct energy conversion, no moving parts (low complexity), and a long lifespan. Power generation for deep space missions and waste heat recovery for automobiles

## Slide 3: Background: TEG design
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Basics of a unit-cell thermoelectric generator design
P- and N-type thermoelectric materials
Conductive interconnectors (Int.)
Heat source and heat sink
String multiple cells together to form a TE modules
Notes: TEGs have direct energy conversion, no moving parts (low complexity), and a long lifespan. Power generation for deep space missions and waste heat recovery for automobiles

## Slide 4: Background: TEG performance
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Figure of merit for TE materials (:
: seebeck coefficient
: electrical conductivity
: thermal conductivity
: mean temperature
Performance rests upon optimizing temperature-dependent material properties and device design
Minimize parasitic radiative transfer across the junction
Radiative heat transfer proportional to
“High performance bulk thermoelectrics via a panoscopic approach” () in Materials Today
Notes: TEGs have direct energy conversion, no moving parts (low complexity), and a long lifespan. Power generation for deep space missions and waste heat recovery for automobiles

## Slide 5: Motivation: View factor
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Radiation view factor (:
A geometric property that quantifies the proportion of diffuse radiation emitted from one surface, , and received by another surface,
Radiation Heat Transfer Rate (:
ε: material emissivity
σ: Stefan-Boltzmann constant
: temperature of emitter
: temperature of receiver
Why do we care?
Accurate heat transfer models
Parasitic radiative transfer that lowers temperature gradient
Notes: TEGs have direct energy conversion, no moving parts (low complexity), and a long lifespan. Power generation for deep space missions and waste heat recovery for automobiles

## Slide 6: Methodology: GPU-accelerated programming and geometry definition
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Graphics Processing Unit (GPU) can achieve massive runtime gains
Thousands of cores that operate in parallel
Computational structure is ideal for repetitive, algebraic tasks
Geometry Input: STL Files
Ubiquitous in CAD software
Robust geometry definition
Example TEG unit-cell defined in STL format
Example STL format
Notes: TEGs have direct energy conversion, no moving parts (low complexity), and a long lifespan. Power generation for deep space missions and waste heat recovery for automobiles

## Slide 7: Methodology: View factor computation
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
View factor:
Every differential area of the emitter surface creates a corresponding ray for each receiver differential area, where the ray vectors are determined by the centroidal locations of each triangle, as determined from the STL file.
View factor summation:
Notes: TEGs have direct energy conversion, no moving parts (low complexity), and a long lifespan. Power generation for deep space missions and waste heat recovery for automobiles

## Slide 8: Methodology: Shadow effect and Möller–Trumbore intersection algorithm
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Shadow effect: a phenomenon that represents any potential ray intersection with a non-participating surface
Reduces view factor magnitude
Möller–Trumbore ray-triangle intersection algorithm:
“Fast, minimum storage ray-triangle intersection” () in Journal of graphics tools
Example of shadow effect
Notes: ANNOTATE THE ABOVE FIGURE WITH U-V PLANE, RAY VECTOR, ETC.

## Slide 9: Methodology: Flow chart
Notes: TEGs have direct energy conversion, no moving parts (low complexity), and a long lifespan. Power generation for deep space missions and waste heat recovery for automobiles

## Slide 10: Methodology: Self-intersection
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Self-intersection : refers to any obstructive surface, intrinsic of either emitting or receiving surface, that need checked by the MT algorithm for possible ray-intersection to properly resolve the view factor
Normally exhibited in curved surfaces
Concentric cylinders that exhibit self-intersection

## Slide 11: Methodology: Self-intersection algorithm
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Self-intersection algorithm: dynamics updates the emitting/receiving surfaces to consider only one tessellation at a time
All other surfaces are considered non-participatory (blocking)
Dynamic geometry partitioning during self-intersection algorithm
Notes: ANNOTATE THE ABOVE FIGURE WITH U-V PLANE, RAY VECTOR, ETC.

## Slide 12: Methodology: Back-face culling
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Back-face culling: a computer graphics technique that refers to the removal of primitive geometries that face away from the camera
In this context, tessellations that “face away” from the emitting tessellation appear clockwise oriented
Increases computational savings and it prevents intersection miscalculations.
Viewers
Culling enabled

## Slide 13: Validation: Analytical studies
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
To validate the program’s effectiveness, numerous geometries with published analytical solutions were inputted and tested
Parallel plates geometry
X/L = Y/L = 1.0
Spatial convergence with increasing mesh density

## Slide 14: Validation: Analytical studies
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
More analytical test cases . . .
Analytical Soln. | Numerical Soln. | Percent Error
0.05573419 | 0.05573420 | 7.05725E-06
Analytical vs. numerical solutions for Z/X = 1.0, Y/X = 1.0
Analytical Soln. | Numerical Soln. | Percent Error
1.00 | 0.9988312 | 0.116872
Analytical vs. numerical solutions for r1 = 0.5 [mm], r2 = 1.0 [mm]
Note: MT, self-intersection, and culling are implemented in concentric spheres

## Slide 15: Results: Single-junction TEG
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Geometrical set-up
As demonstrated, the view factor decreases as H/W increases (with a constant interconnector thickness)
Due to increased prevalence of shadow effect
: Area of p-type TE leg
: Area of n-type TE leg
: Number of junctions
Constant Design Parameters
= 0.1
t = 0.125 [mm]

## Slide 16: Results: Multi-junction TEG, H/W=0.25
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
N=1
N=8
Increase junctions
Constant Design Parameters
= 0.1
H/W = 0.25
Asymptotic behavior observed in the view factor

## Slide 17: Results: Multi-junction TEG, H/W=4.00
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
N=1
N=8
Increase junctions
Constant Design Parameters
= 0.1
H/W = 4.00
Asymptotic behavior observed in the view factor

## Slide 18: Discussion: TEG modeling implications
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Asymptotic curve demonstrates that a realistic model (N>128) could be modeled with a simpler model (N = 16)
View Factor: N = 16 | View Factor: N = 128 | Percent Difference
0.68751517 | 0.69402468 | 0.942356%
View factor values for various junction sizes: θ = 0.1 H/W = 0.25, t = 0.125 [mm].
Number of Junctions | View Factor | Absolute Difference
1 | 0.58177071 | 
2 | 0.637026446 | 0.055256
4 | 0.665832591 | 0.028806
8 | 0.680281868 | 0.014449
16 | 0.68751517 | 0.007233
128 | 0.694024679 | 0.00651
Percent difference between a 16 junction TEG and a 128 junction TEG

## Slide 19: Discussion: Computational Speedup
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
Computational time comparison between the CPU (i9-9980XE) and GPU (i9-9980XE + 2080TI) for a single-junction TEG with θ = 0.1, H/W = 0.25, t = 0.125 [mm]
GPU-acceleration becomes increasingly important as junction size grows

## Slide 20: Conclusion
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion
Outline:
July
GPU-accelerated programming allows for a robust view factor calculator
Shadow effect: MT algorithm
Curved surfaces: self-intersection algorithm, culling enabled
As distance across a TEG hot- and cold-sides increases, the view factor decreases
For constant design parameters, as junction number increases, the view factor behaves asymptotically
Can estimate a large and complex models with simpler models
This methodology facilitates the ability the design and analysis of high-temperature TEGs.

## Slide 21: Acknowledgements:
Outline:
July
Computational resources provided by the Center for Research Computing (CRC) at the University of Pittsburgh
Background
Motivation
Methodology
Validation
Results
Discussion
Conclusion